## Slide 1: Implicit Invocation: The Task Control Architecture
Mike Graves
CS6362 Term Paper
Dr. Lawrence Chung

## Slide 2: Implicit Invocation
+ Supports Extensibility: additional modules can be easily attached
+ Supports Reusability: implicitly invoked modules rely only on triggered events
- Complexity: difficult to control the processing order of implicitly invoked modules. How would this be done?
Note: This illustration is from Dr L. Chung’s CS6362 Lecture Notes at http://www.utdallas.edu/~chung/SA/2.4md4.pdf

## Slide 3: Task Control Architecture (TCA)
History
  Developed by Reid Simmons at Robotics Institute of CMU (1988-1994)
  Funded by NASA to support the Ambler six-legged walker
  Used in over a dozen autonomous systems
Provides a general framework for controlling distributed modules
Consists of distributed modules that communicate via message passing through a central server (a.k.a. central control module )
Uses Implicit Invocation of modules
  Modules do not communicate directly
  Central server multicasts messages to modules that register for them
  Modules may also use execution monitors that register condition-action pairs with server
TCA acts like OS: Supports distributed communication, task decomposition, task sequencing and synchronization, and resource management

## Slide 4: TCA – Component Interaction
Central Control Module
Module 1
Module 2
Module N
Task-specific modules communicate through API library
that accesses a general-purpose reusable central control
module. Control is centralized but data and problem
solving is distributed.

## Slide 5: TCA – Deliberative vs. Reactive Behavior
TCA allows the programmer to easily specify and integrate deliberative and reactive behavior using the TCA API
Deliberative Behavior (i.e., open loop)
  Modules construct hierarchical plans of action using goal and command messages. The Central Control Module maintains plans in task trees dynamically and coordinates the tasks.
  Modules send constrain messages and control parameters with other messages to control the order of task execution. These temporal constraints can be relaxed to allow selective concurrency.
Reactive Behavior (i.e., closed loop)
  Modules send monitor messages that contain a condition-action pair. Central control tests for a condition and takes action if the condition holds. The action alters deliberative plans through the task tree.
  Modules send exception messages and Central Control invokes an exception handler that may alter plans through the task tree.
  Modules may set up a wiretap message to receive a copy of messages sent to another module. This improves module extensibility.

## Slide 6: Task Tree for Procedure Calls
main{
task-1( ); task-2( ); task-3( ); }
task1( ) {
subtask-a( ); subtask-b( ); }
task2( ) {
subtask-c( ); subtask-d( ); subtask-e( ); }
subtask-e( ) {
sub-subtask-x( ); sub-subtask-y( ); }
task3(){
subtask-f( ); subtask-g( ); }
Note: This figure is from TCA Programmers Guide version 8.0

## Slide 7: Task Tree for Asynchronous Invocation
main{
send trigger 1
send trigger 2
send trigger 3
}
handler1( ) {
send trigger a
send trigger b
}
(etc.)
Note: This figure is from TCA Programmers Guide version 8.0

## Slide 8: TCA Task Trees allow Selective Concurrency
Note: This figure is from TCA Programmers Guide version 8.0

## Slide 9: TCA Exception Handling
Separates error recovery algorithms from “normal” behavior
  Since it is impossible to predict all failure modes, exception handling often needs to be added after the primary algorithms have been developed.
  TCA exception handling allows error recovery algorithms to be added without modifying/complicating the original algorithms (i.e., provides program extensibility through incremental, modular adjustments)
Each module registers Exception Handlers and Exception Messages with the Central Module
Each module attaches Exception Handlers to task nodes in the Central Module’s task tree
Modules raise an exception by notifying the Central Module
  The Central Module implicitly invokes the associated Exception Handler’s recovery procedure. This procedure may modify the planned behavior by modifying the task tree.

## Slide 10: TCA Exception Handling
Note: This figure is from TCA Programmers Guide version 8.0

## Slide 11: Ambler Walking Robot
Uses TCA for robot control through efficient interaction of various on-board systems
Designed for planetary exploration (i.e., deep crevices, large boulders, steep slopes, etc..)
Utilizes scanning laser rangefinder for accurate perception of terrain
Remote human operators tell Ambler where to go, not how to get there.
Autonomously builds terrain maps, plans sequence and location of steps, and controls movement, balance, and stability.
The Gait Planner module plans a limited number of steps based on terrain and walking capabilities
The Footfall Planner module determines which steps have best foothold based on previous learning through a neural network.
The Leg Recovery Planner module finally determines how to move each leg without colliding.

## Slide 12: Ambler Component Interaction
Note: This figure is from IEEE Control Systems

## Slide 13: Ambler Task Tree
Note: This figure is from IEEE Control Systems

## Slide 14: Summary
TCA provides many commonly needed control constructs for a complex system that uses the implicit invocation style
  Task Decomposition
  Task Coordination and Synchronization
  Execution Monitoring
  Exception Handling
TCA facilitates incremental development
  Adding new tasks
  Adding new reactive behaviors
  Adding new exceptions
TCA software system is no longer maintained at CMU
  Programmers not familiar with TCA API
  Task Definition Language (TDL) is new research area for Simmons. It is a superset of C++ that includes explicit syntax for task-level control capabilities.

## Slide 15: References
Software Architecture; Perspectives on An Emerging Discipline, M. Shaw, D. Garlan, Prentice Hall, 1996.
Concurrent Planning and Execution for Autonomous Robots, R. Simmons, IEEE Control Systems, 12:1, pp. 46-50, February 1992 (http://www-2.cs.cmu.edu/~reids/papers/tca-ambler.pdf).
Task Control Architecture Programmer's Guide to Version 8.0, R. Simmons, R. Goodwin, C. Fedor, J. Basista, Robotics Institute, Carnegie Mellon University, May 1997 (http://www.wv.inf.tu-dresden.de/Teaching/MobileRoboticsLab/Download/TCA-Manual.pdf ).
http://www-2.cs.cmu.edu/afs/cs/project/TCA/www/TCA-history.html
http://ranier.hq.nasa.gov/Telerobotics_page/Technologies/0710.html