## Slide 1: Computer Architecture
Having studied numbers, combinational and sequential logic, and assembly language programming, we begin the study of the overall computer system.
The term “computer architecture” is just a fancy word for “the way the computer is put together.” It includes:
  How logic circuits (gates, ff’s, and more complex devices like adders, registers, counters, etc.) are arranged in a modern central processor unit (CPU).
  The relation of the CPU to memory, and how CPU/memory interaction occurs.
  How the computer communicates to the user via peripheral devices such as the keyboard, CRT, printer, scanner, etc.

## Slide 2: Course of Study
We will spend most of the remaining lectures discussing the internals of the CPU.
We will devote some attention to the architecture of the modern computer (with emphasis on the MIPS-style architecture, the predominant approach today).
Major topics of study will be:
  Design of the simple arithmetic-logic unit or datapath.
  Design of the CPU control unit.
  Multicycle implementation, a step toward pipeline architecture.
  Overview of pipelining
  Memory management and design in a modern computer.

## Slide 3: The ALU or Datapath
The major components of a computer include:
  The CPU
  Memory
  Peripherals that make the computer useful, such as the disk, printer, and mouse.
The CPU consists of a control unit and the arithmetic/logic unit (ALU).
We first study the ALU.
Computer
Memory
CPU
Peripheral
Devices
Input
Output
Control
ALU

## Slide 4: The Central Processor Unit (CPU)
The major components of the CPU are:
  A unit to load instructions from memory to the CPU.
  The arithmetic-logic unit (ALU) or datapath, to process data.
  Registers to hold arguments and results of ALU processing.
  A control unit to decode instructions and initiate ALU action.
ALU
Instruction Fetch/Decode
Control Unit
Registers

## Slide 5: The ALU
The ALU (Arithmetic-Logic Unit, or Patterson and Hennessy’s datapath) is the “figuring” unit of the computer, providing the calculation capability.
The ALU is connected to storage elements (registers for holding data to be processed and the results of the processing) by data buses.
The ALU processor is normally composed of single-element (one-bit) processors (primarily adders), which are assembled together to form a 32-bit processor, in the case of the MIPS R2000. It also includes some other processing elements (such as a shifter).

## Slide 6: The MIPS Computer: An Example of “Bit-Slicing”
Just as, in Lecture 4, we saw how we could use 1-bit adders to compose a 32-bit adder, the MIPS 32-bit ALU processing unit is simply an amalgam of 32 1-bit processors.
1-Bit Processor
MIPS 32-Bit Processor
Carry/Borrow Out
Sum/Difference Out
AND
OR
1-Bit
Full
Add/
Sub.

## Slide 7: ALU Components
As noted above, the ALU needs other components as well:
  Registers to store arguments and results.
  Buses to carry data from registers to the ALU and results back to the register unit.
  Two memory access units, with associated buses:
    An instruction fetch unit to get instructions from computer memory as needed. This includes a program counter, which always points to the address of the next instruction to be accessed.
    A second path to memory to obtain data to be used in the program and to store data back into memory as required.
  A control unit that tells the ALU what to do (covered later).

## Slide 8: ALU Components
We will use new symbols in the design of the MIPS computer over the next three lectures.
Keep in mind that these are symbols for items you already understand. For instance, the MIPS register block is simply a group of 32-bit registers, and the registers are, in turn, collections of D Flip-Flops.
Thus while the symbols are new, they represent, in general, digital logic with which we are by now quite familiar.
In most cases, the MIPS illustrations shown are from the Patterson and Hennessy book.* Such illustrations are credited as they occur.
* David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 9: ALU Components (3)
Shown above are a number of the symbols for components of the computer that we will be “designing.”
* We note that there is really only a single memory in modern computers, and the terms
“data memory” or “instruction memory” refer only to the channel or pathway into the
common memory unit.
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
PC
Instruction memory* Program counter Adder
Instruction
Memory
Instruction
Address
(32-bit)
Instruction
bits 0-31
New
Address
Current
Address
ADD

## Slide 10: Program Counter Architecture
The program counter (PC) is a register that addresses the next instruction in memory.
Since the PC always points to the “next instruction,” this address must be readily updated.
The usual method is to add 4 to the current address (since the instruction is a 32-bit word and each 32-bit word has an address 4 bytes higher than the last word).
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
Instruction
Memory
PC
ADD
4
32-bit
instruction
32
32
Current instr. address
New instr.
address

## Slide 11: More ALU Components
For the ALU, we need some more components: (1) a register block (group of registers) in which to store operands and results, and (2) the ALU itself, which is primarily combinational logic, as mentioned earlier. Since the ALU is largely an adder plus other logic, we use the adder symbol.
Source Reg. 1 Address
Source Reg. 2 Address
Dest. Reg. Address
Write
Data In
Read Data 1 Out
Read Data 2 Out
Register
Block
32
32
5
5
5
32
ALU
Result
32
32
32
1
Input
Operands
Compare
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 12: ALU Architecture for Processing
In the MIPS CPU, all arguments used in processing are stored in registers.
This requires two buses to route data to the ALU.
All registers are tied to both output buses.
A single input bus carries results back to all 32 registers.
Source Reg. 1 Address
Source Reg. 2 Address
Dest. Reg. Address
Write
Data In
Read Data 1 Out
Read Data 2 Out
Register
Block
5
5
5
32
ALU
Result
32
32
32
1
Compare
Op
code
Fn
code
Rs
Rt
Rd
Sh
amt
Instruction Storage Register
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 13: More ALU Components – Data Memory
In addition to instruction memory, we need data memory.
Now in reality, memory is memory, so when we say “Data memory,” we simply mean we need a path to the single computer working memory to load/store data in load/store instructions.
We color code data memory blue, like instruction memory, to remind us that it is the same memory, only accessed along a different path or bus.
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
Data
Memory
32
32
32
Read
data
Write
data
Address

## Slide 14: The Sign Extender
We remember from studying MIPS instructions and SPIM that many instructions have immediate parts that are 16 bits in length.
The immediate is added to a 32-bit operand (register or PC contents) to create an operand or perhaps a new address, for instance in a branch instruction.
Since the immediate may be + or ─, then to add it to a 32-bit argument, we must sign extend it to 32-bits (as we discussed in the MIPS/SPIM lectures).
The sign extension unit performs this function.
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
Sign
extend
16
32

## Slide 15: Data Bus Connection in a Load Instruction
Note that in a load instruction, the ALU performs the address calculation.
Source Reg. 1 Address
Dest. Reg. Address
Write
Data In
Read Data 1 Out
Read Data 2 Out
Register
Block
5
5
32
ALU
Address
32
32
32
1
Compare
Op
code
16-
bit
imm
Rs
Rt
Instruction Register
Data
Memory
32
Read
data
Write
data
Address
Sign
extend
16
32
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 16: Data Bus Connection in a Store Instruction
In store instructions, the ALU also calculates the memory address.
Source Reg. 1 Address
Source Reg. 2 Address
Write
Data In
Read Data 1 Out
Read Data 2 Out
Register
Block
5
5
ALU
Address
32
32
32
1
Compare
Op
code
16-
bit
imm
Rs
Rt
Instruction Register
Data
Memory
Read
data
Write
data
Address
Sign
extend
16
32
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 17: Branch Instructions
A branch instruction will have one of two results: (1) the branch is not taken, in which case the next instruction is executed (i.e., instruction at address [PC]+4), or (2) the branch is taken, in which case the program counter gets an entirely new address (new address = [PC] + 16-bit immediate from instruction [± 32,768]).
In the first case, we simply use the PC update scheme shown on slide 10 of this lecture. In the second case, the current PC contents (next instruction address, that is, [PC]+4), is added to the 16-bit immediate contents of the instruction to form the new address.
Not only do we need an add function, but also a left shift 2 places (since memory is addressed as bytes, but the 16-bit immediate in the branch instruction is a word address).
This scheme is shown on the next slide.

## Slide 18: Conditional Branch Circuit
Source Reg. 1 Address
Source Reg. 2 Address
Read Data 1 Out
Read Data 2 Out
Register
Block
5
5
ALU
32
32
1
Compare (To branch control)
Op
code
16-
bit
imm
Rs
Rt
Next instruction address (PC+4) from program counter
Branch
address
Sign
extend
16
32
After David A. Patterson and John L. Hennessy,
Computer Organization and Design, 2nd Edition
ADD
Shift
left 2
If branch is taken, 16-bit immediate
in the branch instruction is (1) sign-
extended to 32 bits, (2) shifted left 2
places, and (3) added to current PC
contents.
Branch
instruction

## Slide 19: Jump Instruction Modifications
A jump instruction unconditionally transfers program control to a new location in the program.
The ALU must therefore use the 26-bit immediate address in the instruction to create a new PC address.
This is done by (1) shifting left 2 (to create a proper 28-bit byte address), and (2) adding the upper four PC bits to complete the new 32-bit address.
This new address is then loaded into the program counter as the address of the next instruction to be executed.

## Slide 20: Jump ALU Path
After David A. Patterson and John L. Hennessy,
Computer Organization and Design, 2nd Edition
Source Reg. 1 Address
Source Reg. 2 Address
Read Data 1 Out
Read Data 2 Out
Register
Block
ALU
Shift
left 2
Op
code
26-
bit
imm
26
PC loaded
with jump
destination
address
Jump
instruction
26
28
PC
Upper 4 bits of current
PC address
32

## Slide 21: Combining the Elements to Make a Complete ALU
Over the last ten or so slides, we have “designed” many of the elements that, when assembled, will make up the ALU of our MIPS computer.
We now connect the various sections of the ALU together to produce a final “single cycle” ALU; an ALU that executes one instruction each time the “clock” ticks.
Note that up to now, we have NOT considered any of the Control elements of the ALU; that is, the circuits that interpret the instructions and direct the ALU as to (1) which operation to execute, and (2) what operands or variables to process.
We will cover the so-called Control elements and a multi-cycle implementation in the next lecture.

## Slide 22: Data Buses and ALU Register/Register Functions
ALU
M
U
X
Data
Address
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction
bits 0-31
16 (Bits 0-15)
Result writeback (results of R/R ALU calculation).
32
32
32
32
32
32
5
5
5
Register address buses, each 5 bits wide (Rs & Rt = source registers, Rd = dest. register).
Read Data 1 is one of R/R operands; Read Data 2 may be a second operand in many R/R instructions (or immediate may be used).
MUX selects register
contents or immediate
for R/R instruction
process.
ALU calculation result bypasses
memory for R/R instructions
(MUX chooses result).
ALU processes register data for R/R
instruction (math, logical, shift, etc.).
Input bus
not used.
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 23: Load/Store Functions (Read or Write)
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ALU
M
U
X
Data
Address
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction
bits 0-31
16 (Bits 0-15)
Result writeback (memory data to be loaded in Rd on load instruction).
32
32
32
32
32
32
5
5
5
Register address buses, each 5 bits wide (Rs & Rt = source registers, Rd = dest. register).
Read Data 1 is part of address (added to sign-ext. immediate); Read Data 2 is data to be stored in a store instruction.
MUX selects immediate for address calculation in memory access instruction.
Bypass not used if read/write
instruction (MUX chooses
memory output for loads).
ALU calculates memory address.
Input bus
for data stores.

## Slide 24: Adding the Instruction Fetch Circuit
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ADD
P
C
+4
Instruction
Address
Memory
M
U
X
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
Normal PC update
([PC]+4→[PC])
Memory bypass for R/R results
Result writeback
Note: This is the SAME memory!
32
32
32
32
32
32
5
5
5
Instruction register is not shown.
ALU

## Slide 25: Completing ALU Design
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ALU
P
C
+4
Instruction
Address
Memory
Memory bypass for R/R results
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
M
U
X
32
32
NOTE: Design is complete except for jump instruction path.
32
32
32
32
Normal program counter
update ([PC]+4→[PC])
Branch address
MUX chooses new PC contents depending on whether branch is taken
Result writeback
32
32
32
32
32
32
32
5
5
5
ADD
ADD

## Slide 26: The “Single Cycle” ALU
What we have accomplished in this “ALU design” is to come up with all the processing hardware necessary to implement the MIPS instruction set. Note that we have NOT considered the control circuits (that tell the ALU what to do), and will cover those next lecture.
This basic MIPS processor design is referred to as the “single cycle ALU” (or sometimes the “single cycle CPU”). Why is this?
The reason is that this MIPS CPU (more or less the original implementation of the MIPS instructions) is designed so that ANY instruction can be processed in one cycle of the CPU clock.
Lets consider how this “single cycle” CPU works.

## Slide 27: The “Single Cycle” ALU (2)
Since the ALU is basically combinational logic, the “tick” of the clock governs ALU register behavior, which times the process.
A single clock cycle is from rising to rising or falling to falling edge of the clock. Let us use falling to falling as the reference (remember: a master-slave ff’s output changes on the falling edge of the clock).
Consider what happens when the clock “ticks.”
  The PC is already updated.
  The instruction at memory location [PC] is retrieved. [PC] → [PC+4]
  Instruction is decoded/registers are identified (operands).
  Register output buses send data into ALU; ALU function is identified.
  Register data “flows through” the ALU and is processed.
  (In loads/stores, data memory is accessed for load or store.)
  The memory or ALU results are stored back in a register, if necessary.

## Slide 28: Single Cycle Timing
(Start of cycle) Instruction retrieved into instruction register.
(PC contents updated.)
Instruction decoded and registers accessed.
Register contents gated onto ALU input bus (immediate operands sign-extended and input to ALU).
ALU function identified and ALU result obtained.
ALU results used to access memory location if required.
Memory data written (store) or retrieved (load) if memory access instruction.
Data gated onto register input bus.
(End of cycle) Instruction result stored in designated register if required.
Time
1 clock cycle

## Slide 29: Single-Cycle Timing
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ADD
ALU
P
C
+4
Instruction
Address
Memory
Memory bypass for R/R results
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
M
U
X
32
32
32
32
32
32
Normal program counter
update ([PC]+4→[PC])
Branch address
MUX chooses new PC contents depending on whether branch is taken
Result writeback
32
32
32
32
32
32
32
5
5
5
PC update occurs
early in cycle.
~20% of cycle
~40% of cycle
~60% of cycle
~80% of cycle
100% of cycle
ADD

## Slide 30: ALU Design Summary
We have now seen how the common elements we studied earlier are combined to make the MIPS ALU.
This design is a solid, “single-cycle” implementation that supports the MIPS instruction set we studied in our lectures on assembly language programming.
We will study the control logic for this in the next lecture.
The “single-cycle” implementation has a few drawbacks, however, and we will also discuss in the next lecture how to improve on this design to speed it up considerably.

## Slide 31: “Single-Cycle” ALU Quiz
Why is this architecture called the “single-cycle” architecture?
What is the difference in instruction and data memory?
Why does the CPU need a sign extender?
How is the branch address calculated?
How is the ALU used in load and store instructions?
Why is a MUX needed on one of the ALU inputs?
Why is the jump address field shifted left two bits?

## Slide 32: Quiz Answers
Each instruction takes one clock cycle.
Memory is the same; the paths are different.
You cannot add a 16-bit signed number to a 32-bit signed number.
The 16-bit immediate is sign-extended, left-shifted 2, and added to PC contents.
The ALU calculates the memory address: [Rs] + Imm. → Address
ALU input can be either Rt or a sign-extended immediate.
26-bit jump field is a word address, but memory is byte-addressed.