## Slide 1: The CPU Control Unit
We now have a fairly good picture of the logic circuits in the CPU.
Having “designed” the ALU or datapath so that it can perform the necessary instructions, we now have to do the same thing for the control unit, which decodes instructions and provides direction to the CPU.
The MIPS control unit decodes the six bits on either end of the 32-bit instruction word, that is, the op code and function code* fields, to determine each instruction sequence.
* On R-R instructions.

## Slide 2: The Central Processor Unit (CPU)
In lecture 19, we covered processing elements (blue), including the registers, ALU, and data buses.
We now address the control unit circuitry (red).
  Instruction decoding.
  Control signals to ALU and other control elements.
ALU
Instruction Fetch/Decode
Control Unit
Registers

## Slide 3: Functionality of Control Unit
The control unit determines ALU functions in each instruction and selects operands for the ALU.
The operation code (the left six bits of the instruction) determines the type of operation and in some cases (such as jump instructions) the actual instruction itself.
In the case of register-register instructions, the function code determines the instruction (for example, in the R/R instruction above, the function code 0x 20 means “add”).
00 0000
10 0000
0 1000
0 1001
0 1010
0 0000
Op. code
Shift amt.
$t0
$t1
$t2
Bit 0
Bit 31
Fn. code

## Slide 4: Functionality of Control Unit (2)
As mentioned before, the control unit is a collection of decoders and multiplexers.
The decoded instruction fields tell (1) the ALU what function to perform, (2) what operands to use.
00 0000 0 1000 0 1001 01010 0 0000 10 0000
To shift amount decoder
To dest. reg. decoder
Bit 31
Bit 0
To function code
decoder
To operation code
decoder
To source 2 reg. decoder
To source 1 reg. decoder

## Slide 5: Current Architecture
The ALU control uses instruction bits 0-5 to obtain information about the ALU operation in register-to-register instructions.
Note in the following diagram that some of the decoding is done in the register block, which has the decoding mechanism (as discussed in lecture 8, slides 8 and 9) that identifies source and destination registers in load/store and register/register operations.
The ALU control also has input control lines from the operation code decoder which decodes bits 26-31, and which will be shown later.

## Slide 6: ALU Design with ALU Control Block Shown
ADD
ALU
ADD
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
M
U
X
ALU Control Block (function code/
op code decoder)
32
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 7: ALU Control Block
Function code
(instruction
bits 0-5)
3-bit ALU
control bus
ALU operation
bits from op code
control unit
ALU Control
Block Detail

## Slide 8: Single-Cycle ALU Design with Full Control Blocks
ALU
ADD
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 9: Op Code Control Block Signal Identifier
Op code
decode/
control
block
“RegDst” – Register destination control (MUX input)
“Branch” – Activates branch address change function
“MemRead” – Signals read cycle to data memory circuits
“MemtoReg” – Selects ALU or memory write to register
“ALUOp” (2 lines) – Used with function code in ALU control
“MemWrite” – Signals write cycle to data memory circuits
“ALUSrc” – Selects register and immediate ALU operand
“RegWrite” – Activates write function to register block

## Slide 10: Function of Op Code Control Signals
Signal Name | When Signal = 1 | When Signal = 0
RegDst | Write reg. = $rd (bits 11–15) | Write reg. = $rt (bits 16-20)
Branch | ALU branch compare activated | No branch activated
MemRead | Memory data → write register | No data read from memory
MemtoReg | Memory data → write register | ALU results → write register
ALUOp | NA; lines go to ALU control block | NA; lines go to ALU control block
MemWrite | ALU or register data → memory | No data written to memory
ALUSrc | 2nd ALU operand is immediate (sign-extended instr. bits 0-15) | 2nd ALU operand is from $rt (instruction bits 16-20)
RegWrite | Memory/ALU data → write reg. | No input to register block

## Slide 11: Op Code Control Block Circuitry
Instruction
bits 26-31
TO ALU
control block
“0” “23” “2a” “04”
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 12: Instruction Disposition Showing Destination Units
00 0000 0 1000 0 1001 01010 0 0000 10 0000
Bit 31
Bit 0
To $rd destination register decoder
To $rt source register decoder
To $rs source register decoder
To shift amount decoder (ALU)
ALU
Control
Block
TO ALU Control Block
TO Operation Code Control Block
Op
Code
Control
Block
Register Block
$rs
decode
$rd
decode
$rt
decode
Registers

## Slide 13: Data/control Signal Flow Examples
The following diagrams illustrate the flow of control signals and data in some example MIPS instructions in the single cycle implementation.
The “single cycle” implementation is just a stepping stone to the final MIPS design, but this simpler example has all the features of the more complex final design in terms of data routing and the way in which the control signals determine the specific operation for each given instruction.
Note the data flow in these instructions, and pay special attention to the way some of the combinational devices we studied, such as the decoder and multiplexer, are utilized extensively.

## Slide 14: Start of R-Type Instruction
Instruction
is fetched
ALU
ADD
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 15: Next Step of R-Type Instruction
Registers are identified and needed operands are routed to the ALU and the PC update circuit.
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ALU
ADD
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select

## Slide 16: Third Step of R-Type Instruction
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ALU operation is selected
and performed.
The ALU output is
routed to write
select MUX.
ALU
ADD
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select

## Slide 17: Completion of R-Type Instruction
With the write register line
active, data is written back
to the destination register.
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ALU
ADD
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select

## Slide 18: Load Instruction
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
The load instruction identifies the
register containing the address, the “immediate,” and the write register
ADD
Instr. lines
Data store path
The word addressed in
memory is written back to the identified write register
Immediate
Address data
Read address
ALU
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select

## Slide 19: Branch Instruction
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
PC+4
Addr.
Immediate
Instruction
lines
New PC address
Active
control lines
Register data
ALU
ADD
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select

## Slide 20: Jump Instruction Circuitry Added
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ADD
ALU
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select
M
U
X
32
Left
shift
2
PC+4 (Bits 28-31)
Instruction Bits 0-25
Jump

## Slide 21: Jump Instruction Flow
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
PC+4 data
PC jump data
PC update
Jump control
ALU
ADD
ADD
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select
M
U
X
32
Left
shift
2
PC+4 (Bits 28-31)
Instruction Bits 0-25
Jump

## Slide 22: Exercise 1
On the next slide is a diagram of the complete “single-cycle” preliminary MIPS architecture. On a copy of that diagram:
  Circle every element that contains a decoder.
  Highlight the line that controls the content of the data written back to the destination register.
  Circle the device that allows a 16-bit number to be successfully added to a 32-bit number.

## Slide 23
Print out a copy of this diagram and bring to class.
ALU
ADD
ADD
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select
M
U
X
32
Left
shift
2
PC+4 (Bits 28-31)
Instruction Bits 0-25
Jump

## Slide 24
Decoders
32/16 bit correlation
Rd/Rt Dest.
ALU
ADD
ADD
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select
M
U
X
32
Left
shift
2
PC+4 (Bits 28-31)
Instruction Bits 0-25
Jump

## Slide 25: Making the ALU More Efficient
We have now completed “design” of the basic MIPS R-2000 CPU.
Although a good basic design, it has a serious drawback:
  Our processor is designed so that all instructions complete in one clock cycle.
  While this assures that there is sufficient time to complete any instruction, it also means that one clock period must be long enough to accommodate the longest and most complicated instruction.
  Thus, ALL instructions take as long as the longest instruction.
Since many (most!) instructions in the MIPS architecture take less time to execute than the longest instructions (which are usually the lw memory reference instructions), this means that we are slowing execution of our CPU a large part of the time to accommodate instructions that occur substantially less frequently.

## Slide 26: Comparative Instruction Timing
One clock cycle (= one instruction cycle)
PC update time
Instructions accessed and inputs to register and op decoders stable
Op and function codes decoded and stable
Register outputs (operands) stable
ALU processing complete
Memory accessed and data storage or read complete
Data written to write (destination) register if necessary
Jumps and branches completed about here
Register-register instructions done about here

## Slide 27: Multicycle Implementation
A solution to the single-cycle problem is stated as follows:
  Each instruction has several phases, such as fetch/decode, register selection, ALU processing, etc.
  Instead of using a single clock cycle for the whole instruction, run the clock much faster, and have a single clock cycle for each of the elements or phases of the instruction process.
  Many instructions take fewer phases (for example, jump, branch [the fewest phases], register-register or store instructions), so these instructions execute much faster.
  As most instructions execute faster than the longest instructions (such as lw), the average instruction time will be reduced substantially.

## Slide 28: MIPS Multicycle Concept
Split the processing into five processing segments.
Run the clock much faster (essentially 5X faster!).
Do one instruction segment per clock cycle.
PC updates, branches and jumps take 3 processing segments since they are simpler; they run much faster.
Register-register instructions do not require memory access. They take four instruction segments and finish in about 30% more time than jumps and branches.
Only load memory-access instructions take a full five processing segments (store takes only four), but do not slow down the other instructions to their speed.

## Slide 29: Multicycle Implementation
Instruction
Fetch
Instruction
Decode/
Register
Fetch
ALU
Execution
Memory
Access
(if
required)
Data
Writeback
P
C
Instruction
Memory
Register
Block
Op/Fn
ALU
Data
Memory
Register
Block
1 clock
cycle
1 clock
cycle
1 clock
cycle
1 clock
cycle
1 clock
cycle
Skipped for
store inst.
Skipped for
reg.-reg. inst.
Skipped for jump and
branch instructions
All five segments (five clock cycles) required only for load instructions

## Slide 30: Instruction Cycle Times
Instruction Step | R- Type | Memory Reference | Branches | Jumps
Instruction Fetch | Fetch instruction at address [PC] [PC]→[PC+4] |  |  | 
Instruction Decode /Register Fetch | Register operands fetched; Instruction decoded and control units activate appropriate ALU components |  |  | 
Instruction Execution | ALU output = result of operation on register operand(s) | ALU output is mem. address for load/store | If condition met, [PC]→address output of ALU | PC address is instr. [0-25] (shifted 2 places) + [PC 28-31]
Memory Access or ALU Data Writeback | Logical/shift/math operation result written to dest. reg. | Reg. data stored or data accessed for load to dest. reg. | --- | ---
Memory Data Writeback | --- | Data written to destination register | --- | ---

## Slide 31: Multicycle Advantages
For most instructions, we save 20-40% in clock cycles and our processor is much faster, as mentioned earlier.
Since different parts of the circuit are active only for one cycle at a time, we can use less circuitry because parts of the computer can be reused in different cycles.
  The CPU now needs only one ALU, since it can do the PC update functions prior to the ALU processing.
  Since we access memory for data and instructions in different clock cycles, we only need one path to memory.

## Slide 32: Major Impediment to Multicycle Implementation
Our multicycle processor takes up to 5 clock cycles to complete an instruction.
Each time the clock ticks, part of the instruction is completed, not all of it.
That means that at the end of each clock cycle, we have partial instruction results, but no place to store them!
A first concern is therefore a way to store intermediate data as the instruction winds its way through the various segments of processing.

## Slide 33: Intermediate Results Storage Requirements
ALU
ADD
ADD
Mem. To Reg.
ALU Op.
Branch
Reg. Write
ALU Srce.
Mem. Read
P
C
+4
Instruction
Address
M
U
X
Left
shift
2
Data
Address
Inst.
0-31
M
U
X
Reg. Block
Rs
Rt
Rd
Write
Data
Read
Data 1
Read
Data 2
Sign
Extend
32
Write
Data
Read
Data
Instruction bits 0-31
16 (Bits 0-15)
32
32
32
32
32
32
32
32
32
32
32
32
5
5
5
ALU
Control
Control
Instruction
Memory
Data
Memory
M
U
X
5
6 (Bits 0-5)
Reg. Dest.
Mem. Write
6 (Bits 26-31)
M
U
X
Read
Write
Mem./Reg.
Select
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
Need instruction
storage here
Need operand storage here
Need ALU out storage here
Need
read
data
storage
here

## Slide 34: First-Pass Register Placement
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ALU
ALU
Out
Memory
Address
Memory
Out
Memory
Write
Data
Instruction Register
Instr. 0-15
Memory
Data
Register
Instruction 0-31
Reg. Block
Write Data
Read
Data 1
Read
Data 2
Rs
Rt
Rd
A
B
Inst.
11-15
Instr.
21-25
Instr.
16-20

## Slide 35: Preliminary Multicycle Design Without Control
ALU
ALU
Out
M
U
X
Memory
Address
Memory
Out
Memory
Write
Data
Instruction Register
Instr. 0-15
Memory
Data
Register
Instruction 0-31
Reg. Block
Write Data
Read
Data 1
Read
Data 2
Rs
Rt
Rd
A
B
Ins.
11-
15
4
Sign
Extend
Left
shift
2
M
U
X
Instr. 0-5
Instr.
21-25
Instr.
16-20
M
U
X
Note memory
data path
simplified
ALU now serves
jump/branch
PC update function
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
Our preliminary multicycle processing design is more compact.

## Slide 36: Multicycle Design with ALU Control and PC
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition
ALU
P
C
ALU
Control
ALU
Out
M
U
X
M
U
X
Memory
Address
Memory
Out
Memory
Write
Data
Instruction Register
Instr. 0-15
Memory
Data
Register
Instruction 0-31
Reg. Block
Write Data
Read
Data 1
Read
Data 2
Rs
Rt
Rd
A
B
Ins.
11-
15
4
Sign
Extend
Left
shift
2
M
U
X
Instr. 0-5
Instr.
21-25
Instr.
16-20
PC 0-31
M
U
X
M
U
X

## Slide 37: Completed Multicycle Design
ALU
ALU Op.
Reg. Write
ALU Srce. B
P
C
Left
shift
2
ALU
Control
Control
Reg. Dest.
PC Source
M
U
X
ALU
Out
M
U
X
PC Write Cond.
PC Write
M
U
X
Inst. / Data
Mem. Write
Mem. To. Reg.
Inst. Reg. Write
Mem. Read
ALU Srce. A
Memory
Address
Memory
Out
Memory
Write
Data
Instruction Register
Instr. 26-31
Instr. 0-15
Memory
Data
Register
Instruction 0-31
Reg. Block
Write Data
Read
Data 1
Read
Data 2
Rs
Rt
Rd
A
B
Ins.
11-
15
4
Sign
Extend
Left
shift
2
M
U
X
Instr. 0-5
Instr.
21-25
Instr.
16-20
PC 0-31
M
U
X
M
U
X
PC 28-31
Instr. 0-25
After David A. Patterson and John L. Hennessy, Computer Organization and Design, 2nd Edition

## Slide 38: Multicycle Summary
We have redesigned the MIPS CPU to accommodate a 5-segment instruction partition with each segment taking one clock cycle.
In doing so, instruction execution time was decreased ~ 30-40% and greater efficiency was obtained by reducing the circuitry.
In the next lecture, we will take the final step in the MIPS design and complete the R2000 architecture.
P
C
ALU
Memory
Reg.
A
B
ALU
Op.
Cont.

## Slide 39: Exercise 2
On the Complete Multicycle Design Diagram on the next page, do the following:
  Summarize the inputs into the lower MUX to the ALU.
  Why is the 16-bit sign-extender input directly to the ALU in one case and left-shifted two places in the other?
  Why is the output of the ALU sent directly to the MUX that inputs an instruction address into the PC?

## Slide 40
Print out a copy of this diagram and bring to class.
ALU
ALU Op.
Reg. Write
ALU Srce. B
P
C
Left
shift
2
ALU
Control
Control
Reg. Dest.
PC Source
M
U
X
ALU
Out
M
U
X
PC Write Cond.
PC Write
M
U
X
Inst. / Data
Mem. Write
Mem. To. Reg.
Inst. Reg. Write
Mem. Read
ALU Srce. A
Memory
Address
Memory
Out
Memory
Write
Data
Instruction Register
Instr. 26-31
Instr. 0-15
Memory
Data
Register
Instruction 0-31
Reg. Block
Write Data
Read
Data 1
Read
Data 2
Rs
Rt
Rd
A
B
Ins.
11-
15
4
Sign
Extend
Left
shift
2
M
U
X
Instr. 0-5
Instr.
21-25
Instr.
16-20
PC 0-31
M
U
X
M
U
X
PC 28-31
Instr. 0-25

## Slide 41
Lower MUX Inputs:
4 (to form (PC+4).
Rt contents.
16-bit imm.
L-shifted-2 16-bit imm.
1.
The 16-bit imm. is unshifted when a load/ store address is being calculated ($rs+imm.), but shifted 2 when calculating a branch address (branch address = [PC] ± 32K words, but the PC is a byte address).
2.
The ALU directly calculates the branch address and the next instruction address, as it is the only adder in this architecture.
3.
ALU
ALU Op.
Reg. Write
ALU Srce. B
P
C
Left
shift
2
ALU
Control
Control
Reg. Dest.
PC Source
M
U
X
ALU
Out
M
U
X
PC Write Cond.
PC Write
M
U
X
Inst. / Data
Mem. Write
Mem. To. Reg.
Inst. Reg. Write
Mem. Read
ALU Srce. A
Memory
Address
Memory
Out
Memory
Write
Data
Instruction Register
Instr. 26-31
Instr. 0-15
Memory
Data
Register
Instruction 0-31
Reg. Block
Write Data
Read
Data 1
Read
Data 2
Rs
Rt
Rd
A
B
Ins.
11-
15
4
Sign
Extend
Left
shift
2
M
U
X
Instr. 0-5
Instr.
21-25
Instr.
16-20
PC 0-31
M
U
X
M
U
X
PC 28-31
Instr. 0-25